## Slide 1: PIR-Based Torque Ripple Reduction in PMSM Traction Motors for Electric Vehicles
Presented by
AVS Ravi Teja – 23BEE0077
Course Code: BEEE416L
Course Title: Electric Vehicles

## Slide 2: Objective
This project develops a Proportional-Integral-Resonant (PIR) current controller for an Interior Permanent Magnet Synchronous Motor (IPMSM) used in electric vehicle traction drives to minimize periodic torque ripple caused by cogging torque and inverter dead-time nonlinearity. By introducing resonant compensation at the dominant 6th-harmonic ripple frequency (6ωe), the controller improves torque smoothness and drivetrain NVH performance, particularly during low-speed and regenerative-to-motoring transitions, without increasing the underlying PI controller's bandwidth.
Validate controller performance under simulated variable-speed operation, including electrical-frequency reversals, ensuring the resonant frequency (6ωe) tracks ωe without loss of stability.
Assess robustness to motor parameter variations (Ld, Lq, flux linkage) and current-sensor inaccuracies to confirm reliable ripple suppression under non-ideal conditions.
Quantify torque ripple reduction using FFT-based analysis, benchmarking PIR performance against a conventional PI current controller.